## Slide 1: Job Hazard Analysis Advanced Training Health & Safety
Owner : SIS Corporate Training IN-TQ-HSE-011 (0)
博富特咨询
全面
专业
实用
Notes: This training is to :
make AL employees aware of the requirements and of the indirect & direct risks of their job
help AL employees to carry out a JHA
provide AL employees with JHA tools and examples
provide to all AL employees & contractors* a safe & healthy workplace
The JHA will take into account any safety and hazard studies that have been conducted, accident history and risks specific to processes, products and equipment, and will entail a substantiated analysis of the risks associated with each job the work unit entails and the criticality of these risks. Risk assessment will involve the use of a series of risk assessment tables – one for each work unit job – that specify the risk reduction measures and protective systems selected for each risk.
The individual job risk assessment results will be transferred to the summary document, which thus provides an overall evaluation of the occupational hazards for a given work unit.
Recent legislation and regulations in several countries make job hazard analysis mandatory for all types of activities and work environments.
The management of the summary document, including its dissemination, updating, traceability and availability, must be precisely specified. Failure to comply with this obligation may be subject to criminal prosecution in some countries.

## Slide 2
博富特培训已拥有专业且强大的培训师团队-旗下培训师都拥有丰富的国际大公司生产一线及管理岗位工作经验，接受过系统的培训师培训、训练及能力评估，能够开发并讲授从高层管理到基层安全技术、技能培训等一系列课程。
我们致力于为客户提供高品质且实用性强的培训服务，为企业提供有效且针对性强的定制性培训服务，满足不同行业、不同人群的培训需求。
博富特认为：一个好的培训课程起始于一个好的设计,课程设计注重培训目的、培训对象、逻辑关系、各章节具体产出和培训方法应用等关键问题。
关于博富特

## Slide 3: 工作危害分析 (JHA)
测试 #1
回顾
  需要执行 JHA 的情形 …
  JHA 是团队的努力结果
JHA 分为7 个步骤
  选择要进行JHA的工作
  把工作分为若干个作业活动(工作步骤)  练习
  识别危害  练习
  进行风险分析  练习
  削减风险  练习
  执行行动方案  练习
  定期审查
测试 #2

## Slide 4: JHA 是必需的,当 …
现场有 :
员工
危险
工作/任务/作业 区间

## Slide 5: JHA 是一个团队工作
谁是负责人?
  装置/现场经理 (IMS-GP06)和 HSE经理提供的支持
谁应该参加JHA?
  员工 (强制性)
  直接主管 (强制性)
  人力资源经理
  主管
  医疗和技术专家
  当地社区代表
  第三方专家
  …

## Slide 6: 实施JHA的7个步骤
步骤 1
选择工作
步骤 2
把工作分为若干个作业活动(作业步骤)
步骤 3
识别危害
步骤 4
进行风险评估
步骤 5
降低风险
步骤 6
执行行动计划
步骤 7
定期复审
Notes: Before beginning the risk assessment phase, we recommend setting up a committee to be chaired by the site manager and consisting of the following members who will contribute any risk assessments they may have already made:
Ø Employee representatives
· Present the hazard analyses they have conducted pursuant to local regulations
Ø Physiotherapist
· Presents the entity's health and safety risks
· Presents specific cases of medical surveillance
Ø Employer's representative (specify who for AL, i.e. a site manager, safety manager, etc.)
· Presents the forms submitted to national health insurance funds
· Presents jobs that entail specific risks.
Technical manager
· Presents material safety data sheets (MSDS).
· Presents equipment and machinery risks (this document is sent to labor inspection authorities).
· Presents process risks, particularly for high-risk classified sites, pursuant to government regulations.
· Presents job risk data sheets.
· Presents a generic description of the job(s) of a given work unit (e.g.: operator, driver, filler, welder, customer-service technician, plant shift supervisor, secretary, etc..) in compliance with "competency profiles", if any.
The safety coordinator will present experience feedback, including such information as the types, seriousness and frequency of accidents, for a specific type of activity (e.g. metallurgy, gases, chemicals, etc.) for the Group and for the entity. Broken down by work unit.

## Slide 7: JHA 步骤 1 和 2: 选择工作, 将工作分成若干步骤
参见标准培训材料
观察工作, 和员工交谈
列出观察的已知的工作步骤

## Slide 8: JHA 步骤 2: 将工作分成若干工作步骤
练习 # 3
1) 观看视频及
写出作业员工的工作步骤!
Notes: In a workshop, some fatty cosmetic products are flaked and poured into bags. You will see only some tasks which are part of more complete job.
Answers :
Task 1: Put bags under product feeding hopper
Task 2: Follow the bag feeding process
Task 3: Close bags
Task 4: Load and handle bags from the product feeding hopper to the wood pallet
Task 5: Store bags on wood pallet

## Slide 9: JHA 步骤 3: 识别危害
参见标准培训教材
识别:
  物理和健康危害
    不安全的条件
    不安全的设备
    不安全的工作环境
    不安全的物资
    不安全的组织
  客户或第三方现场物理和健康危害
考虑过去发生的事 (事故,事件,BSV …)

## Slide 10: JHA 步骤 3: 识别危害
练习 # 3
2) 再次观看视频并
识别每一个工作步骤的危害风险 !
Notes: For your information, an operator injured his shoulder while manually lifting bags.
Each bag weighs approximately 20kg
Answers :
Task 1: Put bags under product feeding hopper
Dust (Allergy, asthma, …)  Occupational illness
Task 2: Follow the bag feeding process
Body position/posture  Occupational illness and accidents
Dust while shaking bags  Occupational illness
Product spillage  Accidents
Task 3: Close bags
Body position/posture  Occupational illness and accidents
Heavy Loading and repetitive identical actions  Occupational illness and accidents
Cut with the machine  Accidents
Product spillage  Accidents
Task 4: Loading and Handling bags from the product feeding hopper to the wood pallet
Body position/posture  Occupational illness and accidents
Heavy loading and repetitive identical actions  Occupational illness and accidents
Trips and Falls  Accidents
Bags falling over  accidents
Task 5: Storing bags on wood pallet
Body position/posture  Occupational illness and accidents
Trips, slips and Falls  Accidents
Foot stuck  Accidents
Other risks :
Noise  Occupational illness
Temperature  Occupational illness
Lighting ???  Occupational illness and accidents
Explosive atmosphere (dust)  Accidents
Contact with electrical parts  Accidents
Fire  Accidents
Isolated / single worker  Accidents

## Slide 11: JHA 步骤 4: 进行风险评估
对与工作相关的环境和作业活动的风险予以分析
考虑设计,组织和已经采取的安全措施.
一个职业危害风险的危险程度依赖于两个参数:
  潜在风险产生后果的严重性
  发生伤害和暴露于职业危害风险的概率

## Slide 12: JHA 步骤 4: 进行风险评估
严重程度的评估
  0 – 对作业人员没有影响
  1 – 较小的伤害且没有后遗症
  2 – 严重的伤害但没有后遗症
  3 – 严重的伤害且有后遗症, 部分的或永久的精神的或身体残疾及职业病
  4 – 可能因发生的事故或职业病导致死亡
评估时取风险最严重的后果
Notes: What is a serious injury? as per Riddor (HSE-UK)
  Any fracture, other than to fingers, thumbs or toes
  Any amputation
  Dislocation of the shoulder, hip, knee or spine
  Any loss of sight (whether temporary or permanent)
  A chemical or hot metal burn to the eye or any penetrating injury to the eye
  An injury resulting from electric shock or electrical burn leading to unconsciousness or requiring resuscitation or admittance to hospital for more than 24 hours
  Any other injury:
    leading to hypothermia, heat-induced illness or unconsciousness
    requiring resuscitation
    requiring admittance to hospital for more than 24 hours
  Loss of consciousness caused by asphyxia or exposure to a harmful substance or biological agent
  Acute illness requiring medical treatment or loss of consciousness which results from absorption of any substance by inhalation, ingestion or through the skin
  Any acute illness which requires medical treatment where there is reason to believe that this resulted from exposures to a biological agent or its toxins or infected material

## Slide 13: JHA 步骤 4: 进行风险评估
发生概率评估
  0 – 很不可能发生的事变(event)*
  1 – 不大可能 : 事变是意外的 和/或正常情况下持续非常短的时间
  2 – 很小 : 偶然发生 和/或正常情况下持续时间短
  3 – 可能 : 经常发生 和/或正常情况下持续时间中等
  4 – 频繁 : 重复发生 和/或正常情况下持续时间长
  *事变(Event) = 事故状态(伤害) 或暴露 (疾病)
  注释 :
  暴露 毫无疑问是指慢性接触. 急性接触将作为事故状态来考虑. 无论何种情况,暴露
  必须小于职业接触限值(参考 MSDS).
  首先 考虑你所在单位. 然后, 考虑更大的区域 (全球业务线, 液空集团, 与液空相关
  的外部事件)暴露于危险环境中的概率,从很小到很不可能都要考虑。

## Slide 14: JHA 步骤 4: 进行风险评估
发生概率的评估
  8 小时是时间长度, 或者短期暴露的累计。
  例子:
  OELV : 职业接触限值 (欧盟)
  TLV-TWA :时间加权平均阈限值 (美国)
  *OSHA 标准

## Slide 15: JHA 步骤 4: 进行风险评估
风险危险程度的评估
依据于 GT PR COM 020
纠正措施 :降低风险
  首先, 不可接受风险 ( )
  然后, 中等风险区域 ( )
严重程度 概率 | 0 | 1 | 2 | 3 | 4
4 | 04 | 14 | 24 | 34 | 44
3 | 03 | 13 | 23 | 33 | 43
2 | 02 | 12 | 22 | 32 | 42
1 | 01 | 11 | 21 | 31 | 41
0 | 00 | 10 | 20 | 30 | 40
不可接受的风险区域
中等风险区域
可接受风险区域

## Slide 16: JHA 步骤 4: 进行风险评估
练习 # 3
3) 评估做过的练习中发现的风险!
4) 评估不同的工作步骤中其他的风险!

## Slide 17: JHA 步骤 5: 降低风险
控制风险危害的层次
  我们是否能消除危害? 
  我们是否可以通过下列措施控制风险 
    设计或工程解决办法,
    组织方式和/或程序上的办法?
  我们是否通过下列措施能降低风险造成的后果 
    多人防护设备,
    个体防护装备 (PPE)?
为了达到可接受的残余风险水平 ( )
上面的一个或多个防护控制措施可能是必需的
将防护措施和好的操作实践去比较, 可以检查哪些是相关的。
Notes:   Overall examples :
The actions to take to eliminate or minimize the hazards are:
Eliminate hazardous products (water/solvent)
Change production’s parameters (Production at high temperature/at ambient temperature)
Locate equipment or installations in another place (Liquid CO2 storage close to / far from sewage sludge storage area)
Change the production process
Design or Engineering controls
Substitute by less hazardous products (Change gasket’s material, …)
Design, including collective protection equipment/devices (Safety valves, gear machinery cover, …)
Organize process in order to mitigate risks (Reduce the number of loading/handling tasks, equipment designed with enough space to maintain it …)
Organization and procedure
Alter the sequence or process to reduce the hazard (Does the job have to be performed? Can it be done less often? Can the job be performed in another way? Can you make physical changes to the job? Are the operating and emergency procedures issued and applicable? Are warning signs and barriers in place? Are emergency equipment available?)
Mitigation measures
Collective protective equipment: First choose collective protective equipment (stationary gas detector, room entry prohibition system, …); Define the organization in case of alarms or emergency
Personal Protective Equipment: When exposure to hazards cannot be completely engineered out, and when safe work practices and administrative controls cannot provide sufficient additional protection from exposure, if ( and only if ) the level of residual risk is acceptable (green zone) and personal protective clothing and/or equipment (such as portable detector) could definitively protect the worker, then, PPE may be required. This is the last barrier to reduce consequences (severity) of a hazard

## Slide 18: JHA 步骤 5: 降低风险
核实改进措施是否对作业人员提供充分的防护 (可接受区域)
根据风险降低措施实施行动方案
Severity Probability | 0 | 1 | 2 | 3 | 4
4 | 04 | 14 | 24 | 34 | 44
3 | 03 | 13 | 23 | 33 | 43
2 | 02 | 12 | 22 | 32 | 42
1 | 01 | 11 | 21 | 31 | 41
0 | 00 | 10 | 20 | 30 | 40
现在工作风险处于可接受区域
不可接受的风险区域
中等风险区域
可接受风险区域

## Slide 19: JHA 步骤 5: 降低风险
练习 # 3
5) 观察视频中的灌袋工作,
找到方法
  消除危害
  控制风险
  降低风险危害的后果

## Slide 20: JHA 步骤 6: 实施行动方案
一个好的行动方案常常包括几个互补的行动, 如:
  少数便宜且易做到的改进措施能够很快的完成, 比如
    临时方案, 直到更可靠的控制措施到位, *
    对更可能导致事故或职业疾病的采取永久性方案,
    对可能导致极坏后果的采取永久性方案。
  定期检查,确保防护控制措施在现场有效
  明确责任人和完成时间表
  * 必须遵守IMS-GP13 规定

## Slide 21: JHA 步骤 6: 实施行动方案
行动方案可能涉及到:
  设备或工艺设计的修改
  编制标准作业程序(SOP)或者更新
  培训设计或修改
  培训实施
  多人或个体防护装备的采购
  标识
  将风险告知作业人员 …
优先行动
使用一个实用的文件予以总结
如:在法国,使用Document Unique文件记录实施情况
 |  | 要完成的行动是 |  | 
 |  | 难 | 中等 | 易
风险程度等级 | 不可接受风险区域 | 3 | 2 | 1
 | 中等风险区域 | 4 | 3 | 2
 | 可接受风险区域 | 4 | 4 | 3
Notes: The analysis shall be used to develop mitigation plans and protective measures which include collective and personal protective equipment (PPE), safety instructions, trainings and installation of safety devices such as fire protection systems and extinguishers, man-down systems, warning signs, toxic and flammable gas detectors, disinfection, psychological support etc. These analyses shall also help at facility level to define the needs for:
· Rescue teams and HSE training,
· First aid,
· External assistance, such as emergency medical and/or fire department response.
The HSE Manager shall manage this process at the entity level and ensure, through inspections,
that job hazard analyses are complete and regularly updated as necessary.
Inform and train all employees on JHA conclusions:
  Hazards and hazardous situations,
  Preventive and Corrective measures,
  Rules that employees shall respect
  Feedback organization in case of implementation difficulties
  Safety Emergency Organization

## Slide 22: JHA 步骤 6: 实施行动方案
练习 # 3
6) 发现并实施优先行动!

## Slide 23: JHA 步骤 7: 定期复审
确保风险危害状况是
  相关人员知道的
确保“规定"是
  了解的
  运用的
  有效的
      你可以使用行为安全观察( BSV), 审计, 人体工程学研究, …
应考虑下列事项
  执行规定, 标准操作程序(SOP)遇到的困难, …
  缺少安全装置或程序, …
  法规,规定的变动,
  装置/设施的变更
  工作任务的变化
  任一 “新的” 事件/事故
为改进预防/保护措施
关闭, 定期更新 JHA *
*在许多国家, 法规要求每年复审一次

## Slide 24: JHA记录表单示例
为记录JHA的结果, 可以使用一个excel表格
参见下面表单
Notes: You may continue with the form that you used if the document has the same kind of elements and logic.

## Slide 25: 相关程序文件
液空文件
  GP 06 : OCCUPATIONAL HSE MANAGEMENT
  GT PR HMS 003 : PERSONAL PROTECTIVE EQUIPMENT FOR HOMECARE OPERATIONS
  GT PR HSE 009 : FLAME RETARDANT AND ANTISTATIC PPE CLOTHING
  GT PR HSE 014 : PERSONAL PROTECTION FOR MACHINES
  GT PR ELS 003 : PERSONAL PROTECTIVE EQUIPMENT FOR ELECTRONICS OPERATIONS
  GT-PR-HSE-015 : PERSONAL PROTECTIVE EQUIPMENT TO BE WORN ON ASU, COGEN, HYCO, HPU SITES
  GT PR COM 020 : CRITICALITY MATRIX FOR INDUSTRIAL RISK MANAGEMENT
其他文件
  International Labour Organisation (ILO)
  INRS (Fr)
  HSE-UK (GB)
  http://www.hse.gov.uk/risk/getstart.htm

## Slide 26: 感谢聆听
扫码关注我们
获取第一手安全资讯
如需进一步沟通
↓↓↓
联系我们 | 15250014332 / 0512-68637852
资源整合，产品服务
↓↓↓
公司官网 | http://www.bofety.com/
微信公众号
抖音